Michigan Municipal Workers’ Compensation Fund

Safety and Health Resource Manual

Playground Safety Checklist

| General | OK | NO | Slides | OK | NO |
| --- | --- | --- | --- | --- | --- |
| Equipment stable. No deterioration in footings and joints | ( | ( | There is an 8-ft. obstruction-free zone in front of the exit area and a 6-ft. zone on all sides. | ( | ( |
| Equipment complete, no missing parts. | ( | ( | Slope support frames are straight, and don’t have finger entrapment areas. | ( | ( |
| No warping/bending of members. | ( | ( | Slide is of one-piece construction or connections are of lap-joint construction rather than butt-joint construction. | ( | ( |
| Free from pinch or crush points. | ( | ( | There is clear line-of-straight from top to bottom of the slide. | ( | ( |
| Free from sharp points and corners. | ( | ( | If slide is stainless steel, it is oriented to prevent the sun from heating the slide surface. | ( | ( |
| Concrete footing appropriately buried. | ( | ( |  |  |  |
|  |  |  | Swings |  |  |
| Head/Finger Entrapment |  |  | Swing crossbeam height is 8 ft. or less. | ( | ( |
| No openings between 3/8” to 1”. | ( | ( | Swings are hung 18 inches apart. | ( | ( |
| No openings between 3” to 9”. | ( | ( | Swing seats are free of exposed metal parts or sharp hardware. | ( | ( |
| No angles greater than 55 degrees. | ( | ( | S locks and other connectors are fully enclosed and secure. | ( | ( |
| Hardware |  |  | Spinning Equipment/Merry-Go-Round |  |  |
| Hardware complete, securely attached and without any deterioration. | ( | ( | Platform is level and stays level when unevenly loaded. | ( | ( |
| Fasteners and connecting devices require tools to loosen/remove. | ( | ( | Distance between the bottom of the whirl and ground is less than 3 inches. | ( | ( |
|  |  |  | Equipment is free of open framework and gaps in the central support post. | ( | ( |
| Ladders |  |  |  |  |  |
| Slide ladders are fully enclosed and don’t trap surfacing material. | ( | ( | Sand Boxes |  |  |
| Ladders have slope of 50-75 degrees. | ( | ( | Sand is within the framework and free of foreign matter. | ( | ( |
| Steps are at least 15’ wide. | ( | ( | Box is in a quiet, shady place. | ( | ( |
| Steps are evenly spaced and are between 9” and 11” apart. | ( | ( |  |  |  |
| Stairways and ladders with steps have continuous handrails on both sides. | ( | ( | Maintenance |  |  |
| Step finish is slip-resistant. | ( | ( | Maintenance is regularly scheduled and accomplished. | ( | ( |
|  |  |  | Maintenance personnel understand appropriate safety standards. | ( | ( |
| Play Areas |  |  | Equipment is kept in safe working condition. | ( | ( |
| Free of tripping and falling hazards such as protruding roots and rocks, or other obstacles such as drain pipes. | ( | ( |  |  |  |
| The area has good drainage. | ( | ( |  |  |  |
| There is an 8-ft. fall zone around each piece of equipment, unless otherwise specified. | ( | ( |  |  |  |

Checklists and Tools  – 18-J-1