Inspection Checklist

(Circle the applicable answer Y=Yes, N=No, O=Does Not Apply)

###### EMPLOYEES

Head protection worn in all hazardous areas?

Y	N	O	1.	Full protection hard hats necessary?

Y	N	O	2.	Bump hats sufficient?

Y	N	O	3.	Workers wearing available equipment?

Y  	N 	O	4.	Inspection, cleaning, and maintenance program established?

Eye protection worn in all hazardous areas?

Y 	N 	O	1.	Flying objects controlled such as chips, grindings, dust, pumice, or parts near buffers, grinders, saws, lathes, mills, drills and cutters?

Y  	N  	O	2.	Liquid handling hazards controlled such as splashes or vapors around acids, solvents, oils, or sprays?

Y  	N  	O	3.	Protruding objects at eye level such as machine parts, suspended objects, loose wires, sharp corners?

Y  	N  	O	4.	Cutting and welding flame, sparks, light radiation and side flashes?

Adequate eye protection?

Y  	N  	O	1.	Safety glasses or goggles worn where needed?

Y  	N  	O	2.	Plastic face shields worn where needed; with or without side shields; clear or tinted lens; protects from light, impact, dust, vapors and gases, splash, spark, or glare hazard?

Y  	N  	O	3.	Supervisor enforces eye protection rules?

Y  	N  	O	4.	Inspection, cleaning, and maintenance program established?

Adequate respiratory protection provided?

Y  	N  	O	1.	All equipment of approved type?

Y  	N  	O	2.	Dust masks used for nuisance dusts only?

Y  	N  	O	3.	Cartridge type respirators used only for limited exposure and concentration?

Y  	N  	O	4.	Canister gas masks used only for listed exposure and concentration?

Y  	N  	O	5.	Self-contained breathing apparatus necessary?

Y  	N  	O	6.	Rules for use enforced?

Y  	N  	O	7.	Inspection, cleaning, and maintenance program established?

Hearing protection provided in high noise level areas?

Y  	N  	O	1.	Acceptable noise level.  Ninety decibels for 8 hour exposure?  (Rule of thumb: Can you converse without shouting?)

Y  	N  	O	2.	Can excessive noise be reduced?

Y  	N  	O	3.	Can exposed employees be rotated to quieter jobs?

Y  	N  	O	4.	Ear protection available in areas where noise is above 85 decibels?

Y  	N  	O	5.	Audiometric tests given to employees working in areas above 85 decibels?

Employees maintain safe conditions in their work areas?

Y  	N  	O	1.	Equipment and bench areas clean and orderly?

Y  	N  	O	2.	Ties, loose sleeves, loose jewelry not worn around machines?

Y  	N  	O	3.	Rings or wristwatches not worn when hazardous?

Y  	N  	O	4.	Personal clothing fits well, not loose or baggy?

Y  	N  	O	5.	Personal protection worn as recommended?

Y  	N  	O		a.	Safety goggles, glasses, face shields, safety shoes, head or hearing protection?

Y  	N  	O		b.	Finger, hand or arm protection, respiratory protection?

Y  	N  	O 		c.	Body or  leg protection against oils, water, acids?

### Employees use  “First-Aid” facilities properly?

Y  	N  	O	1.	Medical procedures?  All employees know first-aid location?

Y  	N  	O	2.	All injuries sent for first-aid?

Y  	N  	O	3.	First-aid cabinets clean?  Supplies in good shape?

Y  	N  	O	4.	First-aid cabinets used only for minor injuries?

Y  	N  	O	5.	Are supervisors trained in first-aid?

Y  	N  	O	6.	Someone appointed to administer first-aid when necessary?

Y  	N..	O	7.	Training and other requirements of Bloodborne Pathogens standard met?

Y  	N  	O	8.	Doctor, nurse, hospital, ambulance on call and posted?

MACHINES AND EQUIPMENT

Guarding  provided at all hazardous points on machines and equipment?

Y  	N  	O	1.	Guards over gears, pulleys, belts, chains, saws, grinding wheels, revolving spindles, die openings, arbors, cross slides, etc.?

Y  	N  	O	2.	Guards or 2 hand controls to safeguard employees’ hands?

Y  	N  	O	3.	Projections guarded or distinctively marked?

Y  	N  	O	4.	Grinding, buffing, polishing, and toxic vapor equipment vented?

Y  	N  	O	5.	Exhaust systems maintain airflow of at least 200 ft. per min.?

Y  	N  	O	6.	Does operator stop machine when cleaning, oiling or adjusting?

Y  	N  	O	7.	Power switch “Lock-Out” program followed for equipment repair?

Y  	N  	O	8.	Equipment never used without all guards in place?

Safe conditions maintained around machines and equipment?

Y  	N  	O	1.	Stool or chair, back rest, seat and legs solid?  Correctly adjusted?

Y  	N  	O	2.	Floors or platforms level, solid and clean?

Y  	N  	O	3.	Stocks of parts arranged to leave adequate room for safe work?

Y  	N  	O	4.	General aisle space entirely unobstructed?

Y  	N  	O	5.	Access aisle off the main aisle clear and orderly?

Y  	N  	O	6.	Are main aisles marked with black or white stripes?

Tools maintained in good condition? Do employees use them properly?

1.	Hand Tools

Y  	N  	O	a.	Well designed handles, tight and in good shape?

Y  	N  	O	b.	No broken or worn parts or unnecessary sharp edges?

Y  	N  	O	c.	“Mushroomed” striking surfaces ground off?

Y 	N  	O	d.	Correct tools for the job supplied and properly used?

Y  	N  	O	e.	Tools properly stored to prevent damage, loss or injury?

2.	Machine Tools

Y  	N  	O	a.	Securely stored on or near the machine?

Y  	N  	O	b.	No broken parts?

Y  	N  	O	c.	Not possible for tools to fall into machine?

Y  	N  	O	d.	Each tool of correct type for job intended?

3.	Portable Power Tools

Y  	N  	O	a.	Equipped with 3 prong plugs and/or double insulated case?

Y  	N  	O	b.	Guards in place?

Y  	N  	O	c.	Power cords in good condition - not spliced or taped?

Y  	N  	O	d.	Inspected regularly and maintained?

Y  	N  	O	e.	Employees instructed in safe use?

Is material handling equipment proper, safe and adequate?

1.	Trucks

Y  	N  	O	a.	Proper 2-wheel, 4-wheel lift, power and barrel truck available?

Y  	N  	O	b.	Handles, forks, platforms, lifting mechanisms, cables and wheels in good condition?  Hand guards used on handles?

Y  	N  	O	c.	Used only in areas with sufficient room for safe movement?

Y  	N  	O	d.	Overhead guards for operator protection in place?

Y 	N  	O	e.	Service on schedule?

2.	Elevators

Y  	N  	O	a.	Maximum weight limited posted?

Y  	N  	O	b.	Gates, and/or doors in good condition?

Y  	N  	O	c.	Signals, cables, and other safety devices in good working order?

Y  	N  	O	d.	Will elevator operate with gates raised or door open?

Y  	N  	O	e.	Floor in elevator is good repair?

Y  	N  	O	f.	Properly lighted?

Y  	N  	O	g.	Operating procedure posted?

Y  	N  	O	h.	All openings properly protected?

3.	Hoists

Y  	N  	O	a.	All in good operating condition?

Y  	N  	O	b.	Adequate and safe means for attaching?

Y  	N  	O	c.	Overhead fastenings, cranes or tracks securely anchored?

Y  	N  	O	d.	Positive stop at end of tracks?

Y  	N  	O	e.	Adequate capacity for the loads?

Y  	N 	O	f.	Safety latches on hooks?

Y  	N  	O	g.	Power controls convenient to operate and protected?

4.	Employees handle materials safely?

Y  	N  	O	a.	Do not turn or twist while handling loads?

Y  	N  	O	b.	Get help or proper equipment for too heavy or bulky lifting?

Y  	N  	O	c.	Watch for nails, splinters, sharp edges, etc.?

Y  	N  	O	d.	Observe all safety precautions when transporting materials?

### FIRE HAZARDS

Protection equipment?

Y  	N  	O	1.	Fire extinguishers tagged, checked and accessible?

Y  	N  	O	2.	Extinguishers proper for exposure and properly located?

Y  	N  	O	3.	Are exits marked, lighted and accessible?

Y  	N  	O	4.	Fire escapes adequate, accessible and safe?

Y  	N  	O	5.	Sprinkler valves open and heads clear?

Y  	N  	O	6.	Alarms in working order?

Y  	N 	O	7.	Personnel trained in use of equipment?

Y  	N  	O	8.	“Hot Work” permit used before welding, grinding, cutting, etc.?

Spontaneous ignition

Y 	 N  	O	1.	Are flammables properly handled and stored?

Y  	N  	O	2.	Flammable liquids stored only in UL listed safety cans?

Y  	N  	O	3.	Flammable wastes in closed metal containers and emptied frequently?

Y  	N  	O	4.	Piled material cool, dry, and well ventilated?

Electrical equipment

Y  	N  	O	1.	Makeshift wiring?

Y  	N  	O	2.	Extension cords serviceable?  No spliced connections?

Y  	N  	O	3.	Fuse capacities correct for circuits?

Y  	N  	O	4.	Ground connections clean and tight?

Y  	N  	O	5.	Fuse boxes closed & labeled?

Physical layout

Y  	N 	O	1.	“No Smoking” and “Smoking” areas clearly marked?

Y  	N  	O	2.	Butt containers available and serviceable?

Y  	N  	O	3.	Discarded smoking materials in prohibited areas?

HOUSEKEEPING

Are halls and aisles well lighted, clean and orderly?

Y  	N  	O	1.	Passageways wide enough for safe traffic?  No trip or slip hazards?

Y  	N  	O	2.	Unobstructed by storage, machines, equipment, projections, etc.?

Y  	N  	O	3.	Doors swing correctly?  In good working order?  Not obstructed?

Y  	N  	O	4.	Aisles marked clearly with black or white painted lines?

Are floors in all areas in good condition, clean and orderly?

Y  	N  	O	1.	No materials, parts, scrap, rags, etc. on the floor?

Y 	N  	O	2.	Spilled liquids wiped up immediately?

Y  	N  	O	3.	No loose boards, holes or other trip hazards?

Y  	N  	O	4.	Properly maintained to prevent deterioration?

Y  	N  	O	5.	Openings permanently or temporarily guarded?

Are walls and ceilings clean and in good repair?

Y  	N  	O	1.	Window glass clean?  Not broken?

Y  	N  	O	2.	All fixtures securely fastened to walls or ceilings?

Y  	N  	O	3.	Paint on doors, walls, ceilings, pipes, and ducts in good condition?

Y  	N  	O	4.	Walls not cluttered with calendars, charts, etc.?

Are stairways in good condition?

Y  	N  	O	1.	Tread nosing in good repair?  Landings?  Handrails?

Y  	N  	O	2.	Painted white at top of each flight?  Well lighted?

Y  	N  	O	3.	Entire stairway free of all obstructions, waste, dirt, etc.?

Y  	N  	O	4.	Tread with a 7-11 inch rise-run design?

Y  	N  	O	5.	Standard railing on all open sides and handrails on closed sides?

Are work and storage areas kept clean and orderly at all times?

Y  	N  	O	1.	Trays and boxes at minimum, free of splinters, protruding nails, etc.?

Y  	N  	O	2.	Adequate room for movement at each operation?

Y  	N  	O	3.	Operators’ stools, chairs, equipment and tools safely stored?

Y  	N  	O	4.	Shelves and bins dust free?  Not overloaded?  Neatly arranged?

Y  	N  	O	5.	Materials, supplies, and waste in proper storage or waste containers?

Y  	N  	O	6.	Efficient pest control?  Flies?  Insects?  Mice?

Are restrooms clean and sanitary?

Y  	N  	O	1.	Coat racks properly used?  Items not stored indefinitely?

Y  	N  	O	2.	Lockers clean on top and sides?  Free of odor?

Y  	N  	O	3.	Stools and urinals clean and free of odor?  Each water closet separated by partition and equipped with door?

Y  	N  	O	4.	Wash basins clean?  Used only for personal cleanliness?

Y  	N  	O	5.	Waste sinks clean?  Rinsed after each use?  Area clean?

Y  	N  	O	6.	Dispensing equipment clean?  Good condition?  Well supplied?

Y  	N  	O	7.	Waste containers properly used?  Adequate?

Y  	N  	O	8.	Closed container available in women’s restroom?

Is heating, cooling and ventilation properly controlled?

Y  	N  	O	1.	All areas comfortable?

Y  	N  	O	2.	Dust and vapors properly exhausted?

Are areas outside the building clean and orderly?

Y  	N  	O	1.	Lawns in good shape?  Mowed?  Weeds cut?

Y  	N  	O	2.	Storage in yards neatly arranged?  Is it necessary?

Y  	N  	O	3.	Areas around boiler rooms and incinerators clean and neat?

Y  	N  	O	4.	Parking lots, driveways, sidewalks, streets clean, good condition?

Entry procedure for Permit Required Confined Spaces

Y  	N 	 O	1.	Is an “entry Permit” used before entry is made into silos, bins, tanks, vessels, pits, etc.?

Y  	N  	O	2.	Is a lifeline and observer used during entry?

Y  	N  	O	3.	Is respiratory equipment or other equipment needed for entry?